## Slide 1
Self-driving Model Car
Vision & AI base

## Slide 2
Project Overview
- Summary, Block Diagram
Roles & Responsibilities
- Role of Mine
Specification
- ROS Publisher(keyboard, cam)
- ROS Subscriber(car_control)
- car_control(stm32, usart, Test QT)
Result

## Slide 3
Project Overview SUMMARY
Vision & AI Base Self-driving Model Car
Project Goals 1. Self-driving in Self-produced track(Straight and S Course) 2. Stop at the stop line and Bypass the hurdle Using Image Processing(OpenCV) 3. Recognition of traffic light and sign Using A.I(Machine Learning)
Logitech Camera
360 Laser Distance Sensor LDS-01
NVIDIA JETSON TX2
STM32 F722ZE
Motor Motor ESC
ARM Cortex A57 CPU
Linux
ROS
Middle Ware
Application
Image Processing Machine Learning

## Slide 4
Project Overview HARDWARE DIAGRAM
Vision & AI Base Self-driving Model Car
→ Electric Current
TX2 Battery
USB HERB
Car Battery
ESC
STM32 F722ZE
Logi Camera
LDS Sensor
Brushless Motor
Steering Servo
NVIDIA JETSON XAVIER
NVIDIA JETSON TX2
Logi Camera

## Slide 5
Project Overview HARDWARE DIAGRAM
Vision & AI Base Self-driving Model Car
→ Data
USB
HERB
ESC
STM32 F722ZE
Logi Camera
LDS Sensor
IMU Sensor
Brushless Motor
Steering Servo
NVIDIA JETSON XAVIER
NVIDIA JETSON TX2
Logi Camera

## Slide 6
Jang In Sang
Lee Jun Tae
Jung Ji Won
Lee Mi Reu
Role Sensor(LDS) Data Analysis
Bluetooth Module
ROS Publisher(LDS)
Role
Car(Motor, ECS) Control TX2 ↔ STM32 Communication ROS Publisher(Keyboard Joystick, Image Processing), Subscriber(Application)
Roles & Responsibilities
Vision & AI Base Self-driving Model Car
Role(Software)
Image Processing(OpenCV) Lane, Stop Line detection
And Analysis
Role(Software)
Machine Learning(A.I) ROS Publisher(A.I) And Analysis

## Slide 7
Node/Topic/MSG
Specification Robot OS
Vision & AI Base Self-driving Model Car
Node ‘KEYBOARD’
Topic Name ‘keyboard’
MSG: flaot32[] keyboard
[start(1)/stop(0), steer, speed, speed_before]
Node ‘AI’
Topic Name ‘ai’
MSG: int8 ai
detection(1)/None(0)
Node ‘LDS’
Topic Name ‘lds’
MSG: float32[3] lds
[detection(0)/None(1), angle, distance]
Node ‘CAM’
Topic Name ‘cam’
MSG: float32[] cam
[steer, speed, speed_before]
Node ‘car_control’
Topic Name ‘keyboard’ ‘ai’ ‘lds’ ‘cam’
MSG ‘four_floats’
floatt32[] keyboard
int8 ai
float32[3] lds
float32[] cam
Publisher
Subscriber

## Slide 8
Communication Config.
Specification Robot OS
Vision & AI Base Self-driving Model Car
TX2 Master URI
roscore
192.168.105.4:11311
TX2 Publisher Node
IP : 192.168.105.4
‘KEYBOARD’ ‘LDS’ ‘CAM’
XAVIER Publisher Node
IP : 192.168.105.5
‘AI’
TX2 Subscriber Node
IP : 192.168.105.4
‘car_control’

## Slide 9
Subscriber ‘car_control’
Specification Robot OS
Vision & AI Base Self-driving Model Car
Yes
Keyboard joystick control
car_control speed=0
Yes
keyboard[0]=1
No
ai or lds[0]=1
No
cam control
Serial write

## Slide 10
Publisher ‘CAM’
Specification Robot OS
Vision & AI Base Self-driving Model Car
Original
Split White, Yellow Color

## Slide 11
Publisher ‘CAM’
Specification Robot OS
Vision & AI Base Self-driving Model Car
Gray scale
Smoothing

## Slide 12
Publisher ‘CAM’
Specification Robot OS
Vision & AI Base Self-driving Model Car
Canny edge
ROI

## Slide 13
Publisher ‘CAM’
Specification Robot OS
Vision & AI Base Self-driving Model Car
Hough Transform Avg.
Draw Line(Left, Right, Middle)

## Slide 14
Publisher ‘CAM’
Specification Robot OS
Vision & AI Base Self-driving Model Car
x
y
Pt1(x1, y1)
Pt2(x2, y2)
+
-
Detect left, right line full
Middle Line Slope = (x1-x2)/(y2-y1)
Radian = atan(Middle Line Slope)
Degree = (180 / Pi) * Radian
Steer = Degree * 0.35
Speed = 1
Detect only one line
Detect Left line
Steer = 5, Speed = 1
Detect Right line
Steer = -5, Speed = 1
No Detect line
Steer = 0
Speed = 0

## Slide 15
Publisher ‘KEYBOARD’
Use python pygame
msg.keyboard = [start(1)/stop(0), steer, speed, speed_before]
Press ‘s’key → msg.keyboard[0] = 1 → car_control node keyboard control
Press ‘q’key → msg.keyboard[1] = 0 → car_control node cam control
Press ‘↑’key → speed = speed + 1 (-1 ~ 3)
Press ‘↓’key → speed = speed - 1 (-1 ~ 3)
Press ‘→’key → steer = steer +1 (-15 ~ 15)
Press ‘←’key → steer = steer – 1 (-15 ~ 15)
Specification Robot OS
Vision & AI Base Self-driving Model Car
y
+
-

## Slide 16
NVIDIA JetsonTX2
STM32 F722ZE
Nucleo
PWM Generation
USART ttyACM0
UART3 Receive
USART ttyACM0
UART3 Transmit
Servo
Motor
Brushless
Motor
ESC
PWM(TIM1-Channel1)
3.3V
7.4V 6200mAh Battery
7.4 V
PWM(TIM1-Channel2)
Block Diagram
Specification Car Control
Vision & AI Base Self-driving Model Car

## Slide 17
Specification Car Control
Vision & AI Base Self-driving Model Car
Software Tools
QT Creator – GUI Generation Purpose on NVIDIA Jetson TX2 Development Kit
STM32 CUBE MX – A graphical software configuration tool that allows the generation of C initialization code using graphical wizards
Atollic TrueSTUDIO for STM32 – Extensive STM32 device and board support Video tutorials, documentation and discussion forums available

## Slide 18
STM32 F722ZE Board Specification
CPU : Arm Cortex-M7 core
STM32 microcontroller in LQFP144 package
Ethernet compliant with IEEE-802.3-2002
USB OTG or full-speed device
3 user LEDs
2 push-buttons: USER and RESET
LSE crystal : 32.768 kHz crystal oscillator HSE crystal : 8MHz crystal oscillator
Board connectors : - USB with Micro-AB - Ethernet RJ45
Specification Car Control
Vision & AI Base Self-driving Model Car

## Slide 19
CUBE MX PWM Configuration
Sysclk : 216MHz
PWM pulse period : 20ms(f=50Hz)
Prescaler : 1/432
Counter period : 1/10000
1count period : 20ms/10000=0.002ms
Pulse width count = pulse width / 1count period ex) Servo middle = 760 Stepper neutral = 750
Servo(Steering) Motor
Pulse period : 20ms(f=50Hz)
Max left pulse width : 1.08ms
Max right pulse width : 1.96ms
Middle pulse width : 1.52ms
Brushless(Speed) Motor
Pulse period : 20ms(f=50Hz)
Full reverse : 1ms
Neutral : 1.5ms
Full forward : 2ms
Specification Car Control
Vision & AI Base Self-driving Model Car

## Slide 20
USART Communication
Available on PD8 and PD9 - PD8 : USART3 TX, SB5 ON and SB7 OFF - PD9 : USART3 RX, SB6 ON and SB4 OFF
Can be connected either to ST-LINK or to ST morpho connector.
Specification Car Control
Vision & AI Base Self-driving Model Car

## Slide 21
Steering
760
16 0 도
980
R15(31)
540
L15(15)
-30도
Speed
Neutral : 0
Forward : 1~3 Stage
Reverse : only 1 stage
R/L
Protocol
Steering Left/Right bit
L : 0, R : 1
Steering bit
0(0000)~15(1111) stage
Speed bit
0(000) : neutral
1(001)~3(011) : 1~3 stage forward
4(100) : only 1 stage reverse
Specification Car Control
Vision & AI Base Self-driving Model Car

## Slide 22
UART MSG(Text edit)
Transmitted message with UART
Protocol applied
SPEED(Spin box)
Range : Max 3 ~ Min -1
Combined with Vertical bar
STEER(Spin box)
Range : Max 15 ~ Min -15
Combined with Horizontal bar
NVIDIA Jetson TX2 TestGUI
Specification Car Control
Vision & AI Base Self-driving Model Car

## Slide 23
Result Self Driving Model Car
Vision & AI Base Self-driving Model Car
Project Goals
Self-driving in Self-produced track (Straight and S Course)
Stop at the stop line and Bypass the hurdle Using Image Processing(OpenCV)
Recognition of traffic light and sign Using A.I(Machine Learning)
Project Perfection
Complete
Can’t Bypass the hurdle
Change Object traffic light and sign->cat doll